UVp-2088 Column Anode → Common cathode in row
Row Cathode

http://i0.wp.com/tronixstuff.com/wp-content/uploads/2013/09/max7219_resistor_table.jpg

http://www.planetarduino.org/?cat=432

conect rtc to arduino.
conect  SDA  to Arduino A4.
conect  SCL  to Arduino A5.
conect vcc to  +5v
conect gnd to gnd

http://www.instructables.com/id/Clock-with-termometer-using-Arduino-i2c-16x2-lcd-D/

http://www.sharatronica.com/cd4017.html

Sensor óptico

http://www.hobbytronics.co.uk/mosfet-voltage-level-converter

Placa
Main board
En v0.2 están A0, A1, A2, A3 para botones (en placa A0, A1, A2, A3)
El chip usa los pines 10, 11, 12
Se exportan 2-9 (en placa D2-D9)
13 libre
Botones → En v.0.1 K4 es A0, K3 es A1. http://arduino.cc/en/Tutorial/InputPullupSerial
pinMode(0, INPUT_PULLUP); analogRead(0); (se han cableado a analog)???

TODO
Arreglar conexión masas en V.0.3 para V.0.4
Revisar agujeros batería, demasiado grandes. ELIMINAR
Revisar agujeros switch, demasiado pequeños
Añadir TEA5767 / TDA7330 http://www.vwlowen.co.uk/arduino/bedside-clock/page2.htm
http://nicuflorica.blogspot.ro/2013/06/radio-fm-cu-tea5767-si-arduino-ii.html
http://blog.simtronyx.de/en/simple-fm-stereo-radio-with-a-tea5767-breakout-module-and-an-arduino/
http://nicuflorica.blogspot.ro/2014/11/modul-de-afisare-cu-8-cifre-led-din-7_11.html

Sensor-power
RTC se conecta por I2C SDA (A4) SCL (A5)
Scanning...
I2C device found at address 0x50 !
I2C device found at address 0x68 !
done

BMP180 SDA (A4) SCL (A5) (OK)
DHT11 conecta a D6 (OK)
BOOST (pendiente)

Es posible usar otros con SerialTWI
SPI: 10 (SS), 11 (MOSI), 12 (MISO), 13 (SCK).

Poner también batería?
Cargador? 2 AA

In addition, some pins have specialized functions:
- Serial: 0 (RX) and 1 (TX). Used to receive (RX) and transmit (TX) TTL serial data. These pins are connected to the TX-0 and RX-1 pins of the six pin header.
- External Interrupts: 2 and 3. These pins can be configured to trigger an interrupt on a low value, a rising or falling edge, or a change in value. See the attachInterrupt() function for details.
- PWM: 3, 5, 6, 9, 10, and 11. Provide 8-bit PWM output with the analogWrite() function.
- SPI: 10 (SS), 11 (MOSI), 12 (MISO), 13 (SCK). These pins support SPI communication, which, although provided by the underlying hardware, is not currently included in the Arduino language.
- LED: 13. There is a built-in LED connected to digital pin 13. When the pin is HIGH value, the LED is on, when the pin is LOW, it's off.
The Pro Mini has 8 analog inputs, each of which provide 10 bits of resolution (i.e. 1024 different values). Four of them are on the headers on the edge of the board; two (inputs 4 and 5) on holes in the interior of the board. The analog inputs measure from ground to VCC. Additionally, some pins have specialized functionality:
I2C: A4 (SDA) and A5 (SCL). Support I2C (TWI) communication using the Wire library.
There is another pin on the board:
Reset. Bring this line LOW to reset the microcontroller. Typically used to add a reset button to shields which block the one on the board.

# Protel Gerber Layer Names
GTO - Gerber Top Overlay (silkscreen)
GBO - Gerber Bottom Overlay (silkscreen)
GTL - Gerber Top Signal
GBL - Gerber Bottom Signal
GTS - Gerber Top Solder Mask
GBS - Gerber Bottom Solder Mask
GTP - Gerber Top Paste Mask
GBP - Gerber Bottom Paste Mask
GM1 - Gerber Mechanical 1
GM2 - Gerber Mechanical 2
GM3 - Gerber Mechanical 3
GM4 - Gerber Mechanical 4
GDD - Gerber Drill Drawing
GD1 - Gerber Drill Drawing, Top To Mid 1
GD2 - Gerber Drill Drawing, Mid 1 To Mid 2
GDG - Gerber Drill Guide
GG1 - Gerber Drill Guide, Top To Mid 1
GG2 - Gerber Drill Guide, Mid 1 To Mid 2
GPT - Gerber Top Pad Master
GPB - Gerber Bottom Pad Master
GKO - Gerber Keepout
PO1 - Gerber Panels
REP - Report file
TXT - ASCII NC Drill
DRL - EIA NC Drill
DRR - NC Drill Report
APR - Aperature File

Coin cell holder
http://www.shogyo.com/pdf/ch224-2032lf.pdf